## Slide 1: Little Groot
Providing Brain and sensing ability to plants
Idea
Seeing the movie Guardians of the Galaxy, we thought of why not giving the life to plants, asking for their requirement.
By Team Ravana
On Rajasthan Hackathon 3.0 - Udaipur

## Slide 2: Working
* The plant monitor has a moisture sensor that measures how wet your
plant’s soil is. If the plant needs watering, an LED lights up and blink until the
* plant’s been watered, and the string “Feed me!” is repeatedly sent to your computer.
* When the plant has been watered, the LED switches off and the string “Thank you, Team Ravana!” is sent once to your computer.
* This version of program is for normal plant.
* There are Three conditions according to plant water requirement.
* It also detects the upcoming creatures around it and will start buzzer sound.

## Slide 3
Future Of Groot
Program for different Plant water requirement.
Implementation of Motor and automatic on and off according to question.
Display on Board
Wireless interface
Operating through SMS.
For variable value of Moisture implementation of Transistor.
Usefulness
When you are out of place and time.
For Farmers
To save our upcoming generations
To get an air full of oxygen and reduce pollution.
Thank You.

## Slide 4: Construction
Connect a short jumper wire from the GND pin on the Arduino to slot D15 on the breadboard.
Connect a short jumper wire from the 0 Analog input pin to slot D10 on the breadboard.
Connect the 10K Ohm resistor from slot C15 on the breadboard to slot C10.
Take one of the galvanized nails, and connect the wire attached to it to slot B10.
Connect a short jumper wire from the 5V pin on the Arduino to slot C5 on the breadboard.
Take the other galvanized nail, and connect the wire attached to it to slot B5.